## Slide 2: PLOCTree: A Fast, High-Quality Hardware BVH Builder
Timo Viitanen, Matias Koskela, Pekka Jääskeläinen, Aleksi Tervo, Jarmo Takala
Virtual reality and Graphics Architectures group, www.tut.fi/vga
Tampere University of Technology, Finland
High Performance Graphics 2018, Vancouver, Canada
Sunday, 12 Aug, 2018

## Slide 3: Real-time ray tracing
Long-term goal in computer graphics
Highlight this year: DirectX Raytracing (DXR) API, NVIDIA RTX
Hardware acceleration for real-time ray tracing
  Academic and commercial architectures: ART, Samsung SGRT, PowerVR Wizard, Caustic, TraX, RayCore, RPU, …
Picture by Qutorial / CC-BY-SA
Notes: It has been a long term goal (or pipe dream) in computer graphics to improve the performance of ray tracing to the point where it could be used for high-quality real-time rendering, to bring new visual effects to e.g. Computer games.
Recently it’s increasingly looking like this is going to happen, especially with the launch of RTX and DXR this year. In this conference we’ve already heard several talks and keynotes starting to sketch what sort of visual effects we could get in real time with a limited ray budget.
One related direction of research is to devise hardware accelerators. GPUs already have a lot of fixed hardware for conventional rendering, like rasterizers, TMUs and ROPs, so a bit more for ray tracing might not hurt, and might give us a bigger ray budget. (Some of Nvidias rtx marketing slides sound like nvidia might have something like this, though I have no idea if this is the case)

## Slide 4: Dynamic scene support
Difficulty specific to ray tracing: dynamic scene support
Most interesting scenes have e.g. object insertion, deletion, movement, deformation…
Have to update or rebuild the tree for each frame
This paper proposes a new tree build accelerator to help with dynamic scenes

## Slide 5: Memory traffic is expensive
GPU GFLOPS vs. BW in high-end GPUs
Energy&power are limiting factors even in desktop GPUs
Memory traffic has a high energy cost vs. on-chip compute
Memory bandwidth is scarce: in 10 years GPU compute power has increased ca. 30x and BW by 5x.
~30x
~5x
Notes: ...As a result, the main goal in ray tracing hardware has been to reduce memory traffic.

## Slide 6: Previous work, motivation
(Doyle et al. 2013): Top-down binned SAH sweep builder
(Viitanen et al. 2017): MergeTree LBVH builder
(Nah et al., 2015): HART, BVH refitter
  Restricted to mesh deformations
All based on antiquated algorithms; in software there are newer algorithms that are both fast and high quality
e.g. Parallel Locally-Ordered Construction (PLOC) (Meister and Bittner 2018).
In this work we adapt PLOC to hardware
Build speed
Tree
quality
Binned SAH
LBVH
Recent SW
methods
Notes: The main motivation behind this current work is that there has been tremendous progress in tree build algorithms in the last few years. The previous HW builders are based on algorithms that could now be called antiquated: there are new ones that give both good tree quality and a fast build speed
We found that one recent method in particular was suitable for hardware use.

## Slide 7: PLOC algorithm (Meister and Bittner 2018)
Assign Morton codes to triangles
Sort
Repeatedly:
  Find nearest neighbors
  Merge NN pairs into inner nodes

## Slide 8: PLOC algorithm (Meister and Bittner 2018)
Assign Morton codes to triangles
Sort
Repeatedly:
  Find nearest neighbors
  Merge NN pairs into inner nodes

## Slide 9: PLOC algorithm (Meister and Bittner 2018)
Assign Morton codes to triangles
Sort
Repeatedly:
  Find nearest neighbors
  Merge NN pairs into inner nodes

## Slide 10: PLOC algorithm (Meister and Bittner 2018)
Assign Morton codes to triangles
Sort
Repeatedly:
  Find nearest neighbors in a local window
  Merge NN pairs into inner nodes
Center
element
R=1 local window
Notes: In PLOC the first step is to sort triangles according to Morton codes. In contrast to LBVH which then uses Morton code bits to produce the hierarchy, PLOC uses the Morton order as a proxy for spatial locality. If we search just a small window of neighbors in the Morton order array, we are likely to find the global nearest neighbor, or something good enough.

## Slide 11: PLOC algorithm (Meister and Bittner 2018)
Sorted
input
NN search
R
Notes: After Morton code sorting, the algorithm proceeds as follows. We find local nearest neighbors for each triangle

## Slide 12: PLOC algorithm (Meister and Bittner 2018)
Input
NN search
Merge
Notes: Next we find triangles that are each other’s mutual nearest neighbors, and each such pair a merged into an inner node of the bounding volume hierarchy.

## Slide 13: PLOC algorithm (Meister and Bittner 2018)
Input
NN search
Merge
Compact
Notes: Finally in the original GPU implementation, the output array gets compacted to remove gaps.

## Slide 14: PLOC algorithm (Meister and Bittner 2018)
Input
NN search
Merge
Compact
Sweep 1
Notes: I’ll call one repeat of these steps a sweep

## Slide 15: PLOC algorithm (Meister and Bittner 2018)
Input
NN search
Merge
Compact
NN search
Merge
Compact
Sweep 1
Sweep 2
Notes: Sweeps are repeated until…

## Slide 16: PLOC algorithm (Meister and Bittner 2018)
Sweep 3
Input
NN search
Merge
Compact
NN search
Merge
Compact
NN search
Merge
Compact
Sweep 1
Sweep 2

## Slide 17: PLOC algorithm (Meister and Bittner 2018)
Sweep 3
Input
NN search
Merge
Compact
NN search
Merge
Compact
NN search
Merge
Compact
NN search
Merge
Sweep 1
Sweep 2
Sweep 4
Notes: Finally, the last sweep takes two boxes as input, and merges them into the root node of the tree

## Slide 18: PLOC sweep pipeline
Input
Sliding
window
memory
DME
DME
DME
DME
<
<
<
Distance
metric
evaluators
Comparator
tree
Notes: Next we'd like to design a hardware architecture to do this.
Looking at the algorithm, it's visible from before that each element of the sweep output array only depends on a small, fixed-size range of elements in the input array. Hence we can use a sliding-window memory (familiar from signal processing systems).
The sweep hardware has two parts; the first is going to do find local NNs; the second will do merging and compaction. Here we see the first part

## Slide 19: PLOC sweep pipeline
Input
Sliding
window
memory
DME
DME
DME
DME
<
<
<
Distance
metric
evaluators
Comparator
tree

## Slide 20: PLOC sweep pipeline
Input
Sliding
window
memory
DME
DME
DME
DME
<
<
<
Distance
metric
evaluators
Comparator
tree
Notes: Next, we have hardware units to compute distances of the center element to the other elements in the local window, followed by a comparator tree to find the one with the lowest distance. This gives us a output stream of triangle bounding boxes annotated with the nearest neighbor index.

## Slide 21: PLOC sweep pipeline
Input
Sliding
window
memory
DME
DME
DME
DME
<
<
<
Distance
metric
evaluators
Comparator
tree

## Slide 22: PLOC sweep pipeline
Input
Sliding
window
memory
DME
DME
DME
DME
<
<
<
NN, AABB
buffer
Distance
metric
evaluators
Comparator
tree
Merge
decision
PASS
THROUGH
(not mutual NN)
Output
Notes: Next, we have the second part of the pipeline, that is responsible for merging. To do this, we start with another sliding window with annotated elements. In this one, we can take the center element, make a memory access inside the window to its nearest neighbor, and determine whether they form a pair.

## Slide 23: PLOC sweep pipeline
Input
Sliding
window
memory
DME
DME
DME
DME
<
<
<
NN, AABB
buffer
Distance
metric
evaluators
Comparator
tree
Merge
decision
MERGE
Output

## Slide 24: PLOC sweep pipeline
Input
Sliding
window
memory
DME
DME
DME
DME
<
<
<
NN, AABB
buffer
Distance
metric
evaluators
Comparator
tree
Merge
decision
MERGE
Output

## Slide 25: PLOC sweep pipeline
Input
Sliding
window
memory
DME
DME
DME
DME
<
<
<
NN, AABB
buffer
Distance
metric
evaluators
Comparator
tree
Merge
decision
CONSUME
(already merged)
Output

## Slide 26: PLOC sweep pipeline
Input
Sliding
window
memory
DME
DME
DME
DME
<
<
<
NN, AABB
buffer
Distance
metric
evaluators
Comparator
tree
Merge
decision
CONSUME
(already merged)
Output

## Slide 27: PLOC sweep pipeline
Input
Sliding
window
memory
DME
DME
DME
DME
<
<
<
NN, AABB
buffer
Distance
metric
evaluators
Comparator
tree
Merge
decision
PASS
THROUGH
(not mutual NN)
Output

## Slide 28: PLOC sweep pipeline
Input
Sliding
window
memory
DME
DME
DME
DME
<
<
<
NN, AABB
buffer
Distance
metric
evaluators
Comparator
tree
Merge
decision
MERGE
Output

## Slide 29: PLOC sweep pipeline
Input
Sliding
window
memory
DME
DME
DME
DME
<
<
<
NN, AABB
buffer
Distance
metric
evaluators
Comparator
tree
Merge
decision
CONSUME
(already merged)
Output

## Slide 30: PLOC algorithm
Sweep 3
Input
NN search
Merge
Compact
NN search
Merge
Compact
NN search
Merge
Compact
NN search
Merge
Sweep 1
Sweep 2
Sweep 4
Notes: Finally, the last sweep takes two boxes as input, and merges them into the root node of the tree

## Slide 31: PLOC algorithm
Sweep 3
Input
NN search
Merge
Compact
NN search
Merge
Compact
NN search
Merge
Compact
NN search
Merge
Sweep 1
Sweep 2
Sweep 4
Pipeline so far eliminates the internal memory traffic in a sweep
…But leaves the memory traffic between sweeps

## Slide 32: Multiple pipelines
<
<
<
<
<
<
Memory
Node/leaf
arbiter
Sweep pipeline 1
Sweep pipeline 2
<
<
<
Sweep pipeline 3

## Slide 33: Sweep size
Chart: 
| Toasters | Bunny | Elephant | Cloth | Fairy | Armadillo | Crytek | Conference | Sportscar | Italian | Babylonian | Hand | Dragon | Buddha | Lion
 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
 | 0.65308 | 0.57345 | 0.60963 | 0.64775 | 0.64518 | 0.5833 | 0.60987 | 0.60841 | 0.63752 | 0.61787 | 0.59685 | 0.66679 | 0.75414 | 0.75603 | 0.6725
 | 0.50588 | 0.4194 | 0.45259 | 0.47834 | 0.48736 | 0.43001 | 0.45667 | 0.4453 | 0.5083 | 0.47521 | 0.44956 | 0.49698 | 0.59111 | 0.59611 | 0.51692
 | 0.40921 | 0.32357 | 0.35175 | 0.36481 | 0.37951 | 0.33381 | 0.35368 | 0.33829 | 0.4098 | 0.37125 | 0.34775 | 0.37809 | 0.47029 | 0.47638 | 0.41349
 | 0.33848 | 0.25374 | 0.27848 | 0.28304 | 0.30074 | 0.26328 | 0.2798 | 0.26305 | 0.33479 | 0.29363 | 0.27592 | 0.29267 | 0.37543 | 0.38224 | 0.33472
 | 0.27915 | 0.19876 | 0.22239 | 0.22213 | 0.24117 | 0.20865 | 0.22442 | 0.20782 | 0.27517 | 0.234 | 0.2207 | 0.22676 | 0.30003 | 0.3069 | 0.27227
 | 0.23301 | 0.1558 | 0.1785 | 0.17501 | 0.19641 | 0.16651 | 0.18099 | 0.16662 | 0.227 | 0.18793 | 0.18121 | 0.17697 | 0.2396 | 0.2464 | 0.2226
 | 0.19585 | 0.12227 | 0.14316 | 0.13849 | 0.16091 | 0.13358 | 0.1469 | 0.13614 | 0.18785 | 0.15273 | 0.15025 | 0.13867 | 0.19136 | 0.19783 | 0.18277
 | 0.16318 | 0.096116 | 0.11573 | 0.10954 | 0.13273 | 0.10708 | 0.11956 | 0.11178 | 0.15584 | 0.12593 | 0.12434 | 0.10871 | 0.15277 | 0.1588 | 0.15069
 | 0.13787 | 0.075561 | 0.093303 | 0.086577 | 0.1099 | 0.086328 | 0.097763 | 0.092094 | 0.13011 | 0.10514 | 0.10325 | 0.0849 | 0.12222 | 0.12763 | 0.1246
 | 0.11678 | 0.059168 | 0.075912 | 0.068351 | 0.091565 | 0.069152 | 0.080086 | 0.076427 | 0.10914 | 0.088669 | 0.085889 | 0.066338 | 0.097857 | 0.10258 | 0.10341
 | 0.099542 | 0.046465 | 0.06197 | 0.053844 | 0.076925 | 0.055496 | 0.065868 | 0.063617 | 0.091794 | 0.075331 | 0.071568 | 0.051713 | 0.078366 | 0.082665 | 0.086108
Total work:
ca. 4..5x the
size of the
first sweep
First 3 or 4 sweeps account for ~half of total work
ca. 50..200 sweeps depending on scene

## Slide 34: Multiple sweeps per pipeline
Input
Sliding
window
memory
DME
DME
DME
DME
<
<
<
NN, AABB
buffer
Distance
metric
evaluators
Comparator
tree
Merge
decision
Output
Enlarge sliding-window buffers to fit S windows
Tag all data in pipeline with a sweep index i
Output if i=S-1, otherwise increment i and feedback to input

## Slide 35: Complete system
<
<
<
<
<
<
Sorting
Subsystem
from MergeTree
Memory bus
Node/leaf
arbiter
Sweep pipeline 1 (S=4)
Sweep pipeline 1 (S=32)

## Slide 36: Evaluation
PLOCtree (proposed):
  RTL implementation in SystemVerilog
  RTL simulated builds of 15 test scenes
  Synthesis & power analysis in 28nm FDSOI CMOS, 1V, 25degC, 1GHz
  SRAMs from CACTI-P
  DRAMs from Ramulator, DRAMPower
  SAH tree quality
MergeTree (Viitanen et al. 2017)
  Identical setup
  Assume a free top-level SAH build for extra quality
Top-down SAH (Doyle et al. 2013)
  Modeled DRAM traffic; optimistic energy from DRAMPower
GPU reference LBVH, PLOC
  Run on GTX 1080 Ti, memory traffic with nvprof

## Slide 37
Area breakdown (mm2)
Power breakdown (mW)
Notes: Here is a breakdown of the resulting cell area and power. The main takeaway here is that the proposed hardware only adds around 50% area to the sorting system – but it’s more compute intensive, so ends up accounting for most of on-chip power. The bigger sliding window memory of the second ends up consuming surprisingly much power.

## Slide 38: Comparison
Energy per triangle (nJ)
Area (mm2)
Chart: 
| (Doyle, 2013) | MergeTree | PLOCTree
Logic | 0 | 0.52607 | 2.5205
DRAM | 26.7721 | 8.7984 | 9.6705
Chart: 
| (Doyle, 2013) | MergeTree | PLOCTree
Area | 12.76 | 1.77 | 2.43

## Slide 39
Chart: Runtime (norm. to HW PLOC)
| 2.564360653 | 0.76632960959999996 | 0.66779782369999996 | 0.61637395120000005 | 0.45555825090000002 | 0.47940465739999999 | 0.44015535519999999 | 0.40277521859999998 | 0.4388829635 | 0.41951013320000002 | 0.3937909168 | 0.3896227692 | 0.37774032730000001 | 0.36321651100000002 | 0.35184309969999999
GPU LBVH | 1.7113 | 1.1029 | 1.235 | 1.1356 | 1.2526 | 1.1723 | 1.6072 | 1.9139 | 1.4047 | 2.2035 | 2.0992 | 1.1571 | 1.2155 | 1.2004
GPU PLOC | 1 | 1.009 | 1.0183 | 1.0093 | 1 | 1.0183 | 1.0106 | 1.0116 | 1 | 1 | 0.9899 | 1.0179 | 1 | 1
HW LBVH+SAH | 1.1753 | 1.045 | 1.055 | 1.037 | 1.0194 | 1.0642 | 1.0745 | 1.1977 | 1.1028 | 1.268 | 1.303 | 1.1071 | 1.0982 | 1.1171
HW SAH | 1.0619 | 0.93694 | 0.95413 | 0.9537 | 0.99029 | 0.94495 | 1.1383 | 1.2791 | 0.96262 | 1.0825 | 1.0505 | 0.92857 | 0.91071 | 0.91892
HW PLOC | 1
Proposed
Notes: TODO Selvempi proposed

## Slide 40
Chart: Memory bandwidth (Normalized to HW PLOC)
| 2.2021851629999998 | 2.3670296999999998 | 2.3966605689999998 | 2.5756037649999999 | 2.6203757670000001 | 2.8219955950000002 | 2.979381981 | 2.8880011919999999 | 2.9469348640000002 | 3.0359623529999999 | 3.0696179520000002 | 3.0334662130000001 | 3.0724224250000001 | 3.2144137850000001
GPU LBVH | 1.7113 | 1.1029 | 1.235 | 1.1356 | 1.2526 | 1.1723 | 1.6072 | 1.9139 | 1.4047 | 2.2035 | 2.0992 | 1.1571 | 1.2155 | 1.2004
GPU PLOC | 1 | 1.009 | 1.0183 | 1.0093 | 1 | 1.0183 | 1.0106 | 1.0116 | 1 | 1 | 0.9899 | 1.0179 | 1 | 1
HW LBVH+SAH | 1.1753 | 1.045 | 1.055 | 1.037 | 1.0194 | 1.0642 | 1.0745 | 1.1977 | 1.1028 | 1.268 | 1.303 | 1.1071 | 1.0982 | 1.1171
HW SAH | 1.0619 | 0.93694 | 0.95413 | 0.9537 | 0.99029 | 0.94495 | 1.1383 | 1.2791 | 0.96262 | 1.0825 | 1.0505 | 0.92857 | 0.91071 | 0.91892
HW PLOC | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Proposed

## Slide 41
Chart: Triangle count
| 11140 | 69666 | 84638 | 92230 | 174117 | 212574 | 262267 | 282751 | 300957 | 373536 | 499748 | 654666 | 871306 | 1087474 | 1604054
GPU LBVH | 0.25884 | 0.36749 | 0.40106 | 0.40602 | 0.58405 | 0.69278 | 0.82458 | 0.8503 | 0.93491 | 1.1076 | 1.3705 | 1.7075 | 2.2569 | 2.781 | 3.9762
GPU PLOC | 3.8665 | 3.4907 | 4.334 | 3.9545 | 7.0358 | 6.0139 | 7.1867 | 7.0155 | 7.8037 | 7.5267 | 8.355 | 8.6454 | 13.6141 | 15.0761 | 18.7523
HW LBVH+SAH | 0.1 | 0.5 | 0.6 | 0.7 | 1.1 | 1.4 | 1.7 | 1.9 | 2 | 2.5 | 3.3 | 4.1 | 5.5 | 7 | 10.4
HW SAH | 1 | 3 | 11 | 30
HW PLOC | 0.1 | 0.5 | 0.6 | 0.7 | 1.3 | 1.4 | 1.9 | 2.1 | 2.1 | 2.6 | 3.5 | 4.4 | 6 | 7.7 | 11.3

## Slide 42: Conclusion
Good tradeoff vs. a state-of-the-art GPU SW builder using the same algorithm
  Avg. 3.9x faster, 7.7x less memory traffic
  …given <<1% the area and <10% the maximum memory BW of the GPU
Good speed-area-quality tradeoff vs. previous hardware builders
Getting closer to a builder that might be interesting to put on GPU
It is possible to map a modern fast, high-quality tree build algorithm to hardware with a tiny memory access
Future work: Tree collapsing (large leafs), software implementation
MergeTree presentation at SIGGRAPH tomorrow
  Monday, 13 Aug, 14.00-15.30, West Building, Room 109-110, Vancouver Convention Centre

## Slide 43: Thank you!
e-mail: viitanet@gmail.com
web: www.tut.fi/vga

## Slide 44: PLOC sweep pipeline
Input
Sliding
window
memory
DME
DME
DME
DME
<
<
<
NN, AABB
buffer
Distance
metric
evaluators
Comparator
tree
Merge
decision
Output

## Slide 45: Comparison
Chart: Runtime (norm. to HW PLOC)
| 2.564360653 | 0.76632960959999996 | 0.66779782369999996 | 0.61637395120000005 | 0.45555825090000002 | 0.47940465739999999 | 0.44015535519999999 | 0.40277521859999998 | 0.4388829635 | 0.41951013320000002 | 0.3937909168 | 0.3896227692 | 0.37774032730000001 | 0.36321651100000002 | 0.35184309969999999
GPU LBVH | 1.4133 | 2.2022 | 2.367 | 2.3967 | 2.5756 | 2.6204 | 2.822 | 2.9794 | 2.888 | 2.9469 | 3.036 | 3.0696 | 3.0335 | 3.0724 | 3.2144
GPU PLOC | 1 | 1.009 | 1.0183 | 1.0093 | 1 | 1.0183 | 1.0106 | 1.0116 | 1 | 1 | 0.9899 | 1.0179 | 1 | 1
HW LBVH+SAH | 1.1753 | 1.045 | 1.055 | 1.037 | 1.0194 | 1.0642 | 1.0745 | 1.1977 | 1.1028 | 1.268 | 1.303 | 1.1071 | 1.0982 | 1.1171
HW SAH | 1.0619 | 0.93694 | 0.95413 | 0.9537 | 0.99029 | 0.94495 | 1.1383 | 1.2791 | 0.96262 | 1.0825 | 1.0505 | 0.92857 | 0.91071 | 0.91892
HW PLOC | 1
Chart: Memory bandwidth (Normalized to HW PLOC)
| 2.2021851629999998 | 2.3670296999999998 | 2.3966605689999998 | 2.5756037649999999 | 2.6203757670000001 | 2.8219955950000002 | 2.979381981 | 2.8880011919999999 | 2.9469348640000002 | 3.0359623529999999 | 3.0696179520000002 | 3.0334662130000001 | 3.0724224250000001 | 3.2144137850000001
GPU LBVH | 1.7113 | 1.1029 | 1.235 | 1.1356 | 1.2526 | 1.1723 | 1.6072 | 1.9139 | 1.4047 | 2.2035 | 2.0992 | 1.1571 | 1.2155 | 1.2004
GPU PLOC | 1 | 1.009 | 1.0183 | 1.0093 | 1 | 1.0183 | 1.0106 | 1.0116 | 1 | 1 | 0.9899 | 1.0179 | 1 | 1
HW LBVH+SAH | 1.1753 | 1.045 | 1.055 | 1.037 | 1.0194 | 1.0642 | 1.0745 | 1.1977 | 1.1028 | 1.268 | 1.303 | 1.1071 | 1.0982 | 1.1171
HW SAH | 1.0619 | 0.93694 | 0.95413 | 0.9537 | 0.99029 | 0.94495 | 1.1383 | 1.2791 | 0.96262 | 1.0825 | 1.0505 | 0.92857 | 0.91071 | 0.91892
HW PLOC | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 46: Sweep size
Chart: 
| Toasters | Bunny | Elephant | Cloth | Fairy | Armadillo | Crytek | Conference | Sportscar | Italian | Babylonian | Hand | Dragon | Buddha | Lion
 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
 | 0.65308 | 0.57345 | 0.60963 | 0.64775 | 0.64518 | 0.5833 | 0.60987 | 0.60841 | 0.63752 | 0.61787 | 0.59685 | 0.66679 | 0.75414 | 0.75603 | 0.6725
 | 0.50588 | 0.4194 | 0.45259 | 0.47834 | 0.48736 | 0.43001 | 0.45667 | 0.4453 | 0.5083 | 0.47521 | 0.44956 | 0.49698 | 0.59111 | 0.59611 | 0.51692
 | 0.40921 | 0.32357 | 0.35175 | 0.36481 | 0.37951 | 0.33381 | 0.35368 | 0.33829 | 0.4098 | 0.37125 | 0.34775 | 0.37809 | 0.47029 | 0.47638 | 0.41349
 | 0.33848 | 0.25374 | 0.27848 | 0.28304 | 0.30074 | 0.26328 | 0.2798 | 0.26305 | 0.33479 | 0.29363 | 0.27592 | 0.29267 | 0.37543 | 0.38224 | 0.33472
 | 0.27915 | 0.19876 | 0.22239 | 0.22213 | 0.24117 | 0.20865 | 0.22442 | 0.20782 | 0.27517 | 0.234 | 0.2207 | 0.22676 | 0.30003 | 0.3069 | 0.27227
 | 0.23301 | 0.1558 | 0.1785 | 0.17501 | 0.19641 | 0.16651 | 0.18099 | 0.16662 | 0.227 | 0.18793 | 0.18121 | 0.17697 | 0.2396 | 0.2464 | 0.2226
 | 0.19585 | 0.12227 | 0.14316 | 0.13849 | 0.16091 | 0.13358 | 0.1469 | 0.13614 | 0.18785 | 0.15273 | 0.15025 | 0.13867 | 0.19136 | 0.19783 | 0.18277
 | 0.16318 | 0.096116 | 0.11573 | 0.10954 | 0.13273 | 0.10708 | 0.11956 | 0.11178 | 0.15584 | 0.12593 | 0.12434 | 0.10871 | 0.15277 | 0.1588 | 0.15069
 | 0.13787 | 0.075561 | 0.093303 | 0.086577 | 0.1099 | 0.086328 | 0.097763 | 0.092094 | 0.13011 | 0.10514 | 0.10325 | 0.0849 | 0.12222 | 0.12763 | 0.1246
 | 0.11678 | 0.059168 | 0.075912 | 0.068351 | 0.091565 | 0.069152 | 0.080086 | 0.076427 | 0.10914 | 0.088669 | 0.085889 | 0.066338 | 0.097857 | 0.10258 | 0.10341
 | 0.099542 | 0.046465 | 0.06197 | 0.053844 | 0.076925 | 0.055496 | 0.065868 | 0.063617 | 0.091794 | 0.075331 | 0.071568 | 0.051713 | 0.078366 | 0.082665 | 0.086108
Chart: 
Toasters | 1 | 0.65308 | 0.50588 | 0.40921 | 0.33848 | 0.27915 | 0.23301 | 0.19585 | 0.16318 | 0.13787 | 0.11678 | 0.099542 | 0.084283 | 0.071179 | 0.05951 | 0.050893 | 0.043533 | 0.037609 | 0.032493 | 0.028274 | 0.024953 | 0.022081 | 0.019926 | 0.018221 | 0.016157 | 0.013823 | 0.012387 | 0.01131 | 0.010143 | 0.0091554 | 0.0078988 | 0.0067319
Bunny | 1 | 0.57345 | 0.4194 | 0.32357 | 0.25374 | 0.19876 | 0.1558 | 0.12227 | 0.096116 | 0.075561 | 0.059168 | 0.046465 | 0.036747 | 0.02924 | 0.023024 | 0.018129 | 0.014412 | 0.011512 | 0.0089857 | 0.0071627 | 0.0056125 | 0.0044067 | 0.0034163 | 0.0026699 | 0.002067 | 0.0016077 | 0.0012201 | 0.00096173 | 0.00077513 | 0.00064594 | 0.00051675 | 0.00037321
Elephant | 1 | 0.60963 | 0.45259 | 0.35175 | 0.27848 | 0.22239 | 0.1785 | 0.14316 | 0.11573 | 0.093303 | 0.075912 | 0.06197 | 0.050297 | 0.041152 | 0.033744 | 0.027541 | 0.022401 | 0.018301 | 0.014958 | 0.012323 | 0.010066 | 0.0083414 | 0.0068527 | 0.0057067 | 0.0047733 | 0.0040289 | 0.00332 | 0.0027647 | 0.0023866 | 0.0020204 | 0.0016895 | 0.0014532
Cloth | 1 | 0.64775 | 0.47834 | 0.36481 | 0.28304 | 0.22213 | 0.17501 | 0.13849 | 0.10954 | 0.086577 | 0.068351 | 0.053844 | 0.042535 | 0.033763 | 0.026933 | 0.02136 | 0.016903 | 0.013206 | 0.010452 | 0.0083704 | 0.0066573 | 0.0052803 | 0.0042286 | 0.0033503 | 0.0026672 | 0.0021793 | 0.0017673 | 0.0013878 | 0.0011385 | 0.00092161 | 0.00073729 | 0.00058549
Fairy | 1 | 0.64518 | 0.48736 | 0.37951 | 0.30074 | 0.24117 | 0.19641 | 0.16091 | 0.13273 | 0.1099 | 0.091565 | 0.076925 | 0.064841 | 0.054567 | 0.046141 | 0.039324 | 0.0335 | 0.028533 | 0.024346 | 0.020888 | 0.01785 | 0.015306 | 0.013141 | 0.011446 | 0.0099646 | 0.0086666 | 0.0075581 | 0.0066162 | 0.0058064 | 0.0050713 | 0.0044912 | 0.0039973
Armadillo | 1 | 0.5833 | 0.43001 | 0.33381 | 0.26328 | 0.20865 | 0.16651 | 0.13358 | 0.10708 | 0.086328 | 0.069152 | 0.055496 | 0.04469 | 0.036138 | 0.029458 | 0.024053 | 0.019509 | 0.015924 | 0.012955 | 0.010523 | 0.0086276 | 0.0071269 | 0.0058662 | 0.0047795 | 0.0038763 | 0.0031095 | 0.0025121 | 0.0020416 | 0.0016888 | 0.0013595 | 0.001129 | 0.00092203
Crytek | 1 | 0.60987 | 0.45667 | 0.35368 | 0.2798 | 0.22442 | 0.18099 | 0.1469 | 0.11956 | 0.097763 | 0.080086 | 0.065868 | 0.05449 | 0.045114 | 0.037672 | 0.031784 | 0.027011 | 0.023129 | 0.019854 | 0.017017 | 0.01468 | 0.012617 | 0.010943 | 0.0094941 | 0.0082664 | 0.0071492 | 0.0062227 | 0.0054601 | 0.004728 | 0.0041523 | 0.0036756 | 0.0032181
Conference | 1 | 0.60841 | 0.4453 | 0.33829 | 0.26305 | 0.20782 | 0.16662 | 0.13614 | 0.11178 | 0.092094 | 0.076427 | 0.063617 | 0.053506 | 0.045244 | 0.038365 | 0.032809 | 0.028201 | 0.024435 | 0.021291 | 0.018688 | 0.016456 | 0.014628 | 0.013008 | 0.011636 | 0.010437 | 0.0093332 | 0.0083677 | 0.0074411 | 0.0065923 | 0.0058531 | 0.0051175 | 0.0043536
Sportscar | 1 | 0.63752 | 0.5083 | 0.4098 | 0.33479 | 0.27517 | 0.227 | 0.18785 | 0.15584 | 0.13011 | 0.10914 | 0.091794 | 0.077592 | 0.065943 | 0.056486 | 0.048409 | 0.041694 | 0.036082 | 0.031078 | 0.026811 | 0.023229 | 0.020029 | 0.017318 | 0.014992 | 0.013009 | 0.011301 | 0.0098984 | 0.0086524 | 0.0074961 | 0.0065159 | 0.0057151 | 0.005024
Italian | 1 | 0.61787 | 0.47521 | 0.37125 | 0.29363 | 0.234 | 0.18793 | 0.15273 | 0.12593 | 0.10514 | 0.088669 | 0.075331 | 0.064136 | 0.054648 | 0.046496 | 0.039538 | 0.033638 | 0.028562 | 0.024078 | 0.020346 | 0.017067 | 0.014341 | 0.012109 | 0.010208 | 0.0086096 | 0.0071988 | 0.0060262 | 0.0049741 | 0.0040933 | 0.0033651 | 0.0028056 | 0.0023318
Babylonian | 1 | 0.59685 | 0.44956 | 0.34775 | 0.27592 | 0.2207 | 0.18121 | 0.15025 | 0.12434 | 0.10325 | 0.085889 | 0.071568 | 0.059398 | 0.049255 | 0.040957 | 0.033909 | 0.028094 | 0.023214 | 0.019006 | 0.015588 | 0.012778 | 0.010453 | 0.0085283 | 0.0070055 | 0.0057609 | 0.0047704 | 0.003964 | 0.0032596 | 0.0026874 | 0.0022071 | 0.0018149 | 0.0014888
Hand | 1 | 0.66679 | 0.49698 | 0.37809 | 0.29267 | 0.22676 | 0.17697 | 0.13867 | 0.10871 | 0.0849 | 0.066338 | 0.051713 | 0.04045 | 0.031578 | 0.024683 | 0.019334 | 0.015188 | 0.011834 | 0.0092627 | 0.0072602 | 0.0056624 | 0.0044465 | 0.0034674 | 0.0026869 | 0.0021095 | 0.0016222 | 0.0012648 | 0.0010066 | 0.0007943 | 0.00061253 | 0.00048574 | 0.00037118

## Slide 47: Area & Power breakdown

## Slide 49: LBVH algorithm (Meister and Bittner 2018)
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111

## Slide 50: PLOC algorithm (Meister and Bittner 2018)

## Slide 51
Chart: Memory bandwidth (Normalized to HW PLOC)
| 2.2021851629999998 | 2.3670296999999998 | 2.3966605689999998 | 2.5756037649999999 | 2.6203757670000001 | 2.8219955950000002 | 2.979381981 | 2.8880011919999999 | 2.9469348640000002 | 3.0359623529999999 | 3.0696179520000002 | 3.0334662130000001 | 3.0724224250000001 | 3.2144137850000001
GPU LBVH | 1.7113 | 1.1029 | 1.235 | 1.1356 | 1.2526 | 1.1723 | 1.6072 | 1.9139 | 1.4047 | 2.2035 | 2.0992 | 1.1571 | 1.2155 | 1.2004
GPU PLOC | 1 | 1.009 | 1.0183 | 1.0093 | 1 | 1.0183 | 1.0106 | 1.0116 | 1 | 1 | 0.9899 | 1.0179 | 1 | 1
HW LBVH+SAH | 1.1753 | 1.045 | 1.055 | 1.037 | 1.0194 | 1.0642 | 1.0745 | 1.1977 | 1.1028 | 1.268 | 1.303 | 1.1071 | 1.0982 | 1.1171
HW SAH | 1.0619 | 0.93694 | 0.95413 | 0.9537 | 0.99029 | 0.94495 | 1.1383 | 1.2791 | 0.96262 | 1.0825 | 1.0505 | 0.92857 | 0.91071 | 0.91892
HW PLOC | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 52
Chart: Runtime (norm. to HW PLOC)
| 2.564360653 | 0.76632960959999996 | 0.66779782369999996 | 0.61637395120000005 | 0.45555825090000002 | 0.47940465739999999 | 0.44015535519999999 | 0.40277521859999998 | 0.4388829635 | 0.41951013320000002 | 0.3937909168 | 0.3896227692 | 0.37774032730000001 | 0.36321651100000002 | 0.35184309969999999
GPU LBVH | 1.7113 | 1.1029 | 1.235 | 1.1356 | 1.2526 | 1.1723 | 1.6072 | 1.9139 | 1.4047 | 2.2035 | 2.0992 | 1.1571 | 1.2155 | 1.2004
GPU PLOC | 1 | 1.009 | 1.0183 | 1.0093 | 1 | 1.0183 | 1.0106 | 1.0116 | 1 | 1 | 0.9899 | 1.0179 | 1 | 1
HW LBVH+SAH | 1.1753 | 1.045 | 1.055 | 1.037 | 1.0194 | 1.0642 | 1.0745 | 1.1977 | 1.1028 | 1.268 | 1.303 | 1.1071 | 1.0982 | 1.1171
HW SAH | 1.0619 | 0.93694 | 0.95413 | 0.9537 | 0.99029 | 0.94495 | 1.1383 | 1.2791 | 0.96262 | 1.0825 | 1.0505 | 0.92857 | 0.91071 | 0.91892
HW PLOC | 1
Notes: TODO Selvempi proposed

## Slide 53
Area breakdown (mm2)
Power breakdown (mW)