## Slide 1: Patch Textures: Hardware Implementation of Mesh Colors
Ian Mallett Larry Seiler Cem Yuksel
2019
Utah Graphics

## Slide 2: Textures
Textures . . . Have Problems

## Slide 3: Textures . . . Have Problems
Artist must make mapping
Notes: Harp on this slide a lot

## Slide 4: Textures . . . Have Problems
Distortion
Seams

## Slide 5: Textures . . . Have Problems
Wasted space

## Slide 6: Textures . . . Have Problems
Incorrect mipmap reduction

## Slide 7: Textures . . . Have Problems
Incorrect anisotropic filters

## Slide 8: Textures . . . Have Problems
Local resolution adjustment means remaking texture and mapping

## Slide 9: Textures . . . Have Problems
Artist must make mapping
Notes: Harp on this slide a lot

## Slide 10: Lots of Different Approaches . . .
(Figure [Yuksel et al. 2019])
What does industry actually use?

## Slide 11: Texture Data Living on Surfaces!
Ptex and Mesh Colors

## Slide 12: Texture Data Living on Surfaces!
Film uses texture data directly on surfaces
  Much easier to model!
  Get all the rendering benefits too
Ptex widely (sometimes exclusively) used
Mesh Colors has also been used in production

## Slide 13: Mesh Colors and Ptex
(Figure modified from [Burley and Lacewell 2008] and [Yuksel et al. 2019])
Every model has a list of patches, each with its own separate texture.

## Slide 14: Mesh Colors and Ptex
(Figure modified from [Burley and Lacewell 2008] and [Yuksel et al. 2019])
Notes: Mention generated with Ptex.
Without getting into detail right now, this minor detail makes implementing Mesh Colors in hardware easier, so in this work, we concentrate on Mesh Colors.

## Slide 15: Mesh Colors and Ptex
(Figures Yuksel et al. 2019)

## Slide 16: Mesh Colors or Ptex . . . In Realtime?
Possible [McDonald 2013], [Yuksel et al. 2010], …
Still less-practical than 2D textures due to SW (or SW+HW) implementation:
  Software is much-slower than hardware!
  Complicated to emulate filtering functionality
  Implementation limitations

## Slide 17: Mesh Color Textures [Yuksel 2017]
Implements Mesh Colors using standard 2D textures
  Almost as fast as 2D textures for simple filtering
  Added shader complexity
  Complicated implementation
  Anisotropic filtering problematic
What if the required HW changes to implement directly were small?

## Slide 18: Our Contribution
We show that implementing Mesh Colors on existing GPUs would require minimal HW changes
Introduce “patch texture” representation—this is what makes the required HW changes minor!
Can leverage existing storage!
Can leverage existing filtering HW!
Edge-crossing unnecessary
Similar performance expected

## Slide 19: Patch Textures
Standard 2D Texture
Set of Patch Textures
Unlike in Mesh Colors, in a Patch Texture, edge and corner data is duplicated, not shared with neighbors.
Notes: Mention quads bilinearly filtered, and

## Slide 20: Patch Textures
Standard 2D Texture
Set of Patch Textures
Individual Patch Texture

## Slide 21: Patch Textures
No restriction on resolution is imposed, but if 2n+1 on a side, Smooth filtering between neighbors is possible.
Individual Patch Texture

## Slide 22: Patch Textures
0
1
2
3
4
0
1
2
3
4
0
¼
½
¾
1
0
¼
½
¾
1
(u,v) and (s,t) coordinates in a patch texture

## Slide 23: Patch Textures
0
1
2
3
4
0
1
2
3
4
0
¼
½
¾
1
0
¼
½
¾
1
(u,v) and (s,t) coordinates in a patch texture
0
1
2
3
4
0
1
2
3
4
0
¼
½
¾
1
0
¼
½
¾
1
Patch Texture (u,v) and (s,t)
2D Texture (u,v) and (s,t)
Notes: Explain that uv/st is unnormalized/normalized

## Slide 24: Patch Texture Storage
Very similar to standard 2D textures

## Slide 25: Patch Texture Storage (Mipmaps)
Very similar to standard 2D textures
Most GPUs store in e.g. 4⨯4 tiles
  If mesh textures are 2n+1 on a side, requires padding

## Slide 26: Patch Texture Storage (Mipmaps)
Power-of-two 2D textures fit nicely in memory

## Slide 27: Patch Texture Storage (Mipmaps)
2n+1 patch textures require padding (a few %)

## Slide 28: Patch Texture Storage (Triangular Patches)
Triangular patch textures do not map nicely to 2D storage
Not necessarily a problem
  Quad-dominant meshes standard
  Patch textures typically small
Clever workarounds exist (though require more HW changes)
Wasted space?

## Slide 29: Patch Texture Storage (Triangular Patches)
Slice

## Slide 30: Patch Texture Storage (Triangular Patches)
Filtering can require values outside triangle to be defined.
Extra defined texels Ref. [Yuksel 2017]
Slice

## Slide 31: Filtering (Quadrilateral Patches)
Exactly the same as for 2D textures!
  (Except we don’t need the half-texel shift of 2D textures for (s,t)↦(u,v) conversion.)
2D Texture
Quad Patch Texture

## Slide 32: Filtering (Triangular Patches)
Triangular patches use barycentric filtering
Many possible ways to tweak existing logic so that it can implement this
Mostly, just pass 0 in some places (see paper)

## Slide 33: Anisotropic Filtering
Same process as for 2D textures
However, we now have the chance to detect patch boundaries!

## Slide 34: Anisotropic Filtering (Patch Boundaries)
What to do about out-of-patch samples?

## Slide 35: Anisotropic Filtering (Patch Boundaries)
“Right” thing is to tra- verse to neighbor patch
This is expensive (an indirection)

## Slide 36: Anisotropic Filtering (Patch Boundaries)
Clamping the points to the edge changes the filter shape.

## Slide 37: Anisotropic Filtering (Patch Boundaries)
Clipping the filter is a simple alternative.

## Slide 38: Anisotropic Filtering (Patch Boundaries)
If multisampling is used, the on-screen result can be similar to the correct filter (see [Yuksel et al. 2010], [Toth 2013])

## Slide 39: Anisotropic Filtering Comparison
Any approach is acceptable
  None of the methods reveal the edges
  Ground truth not expected without edge-crossing
This is because not filtering across edges, like in 2D textures

## Slide 40: Anisotropic Filtering Comparison
Patch Edges
Ground Truth

## Slide 41: Anisotropic Filtering Comparison
Patch Edges
Clamped

## Slide 42: Anisotropic Filtering Comparison
Patch Edges
Clipped

## Slide 43: Anisotropic Filtering Comparison
Patch Edges
Ground Truth

## Slide 44: Anisotropic Filtering Comparison
Patch Edges
Clamped+MSAA

## Slide 45: Anisotropic Filtering Comparison
Patch Edges
Clipped+MSAA

## Slide 46: Proof of Concept
Implemented all algorithms in GPU renderer

## Slide 48: Conclusion
Implementing Mesh Colors requires only minimal changes to existing GPU hardware
Takeaway for vendors: go implement it already! 

## Slide 49: Questions
preprint
2019
Utah Graphics

## Slide 50: Why is it Harder with Ptex?
Ptex and Mesh Colors have minor theoretical differences (they are duals of each-other), but this leads to significant difficulty in-practice.
Main problem is that edge-crossing is required for correct filtering in Ptex.

## Slide 51: Why is it Harder with Ptex?
Data from neighbor required for correct bilinear filter near edge.

## Slide 52: Why is it Harder with Ptex?
Unclear how to correctly filter here. Different solutions, all involving edge-crossing. This means substantial HW changes!
???

## Slide 53: Why is it Harder with Ptex?
Duplicating edge data avoids crossing, but is inconsistent.

## Slide 54: Filtering (Quadrilateral Patches)

## Slide 55: Filtering (Triangular Patches)